## Slide 1
Welcome!
We will be starting very soon…

## Slide 2: Agenda:
Overview of BLE and Capabilities
Developing Accessories
Connectivity though the Pet Tutor App
  - Submitting to the Pet Tutor mini-app store
iOS App Development for Pet Tutor

## Slide 3: Overview:
BLE and its Capabilities:
Very low power connectivity
Wireless connectivity to device from Mac, PC, Phone, Tablets (even wireless programming)
Wireless range between 50-120ft
Constantly Evolving Eco System
  Direct connection to the internet via built in IP stacks in upcoming version
  http://www.bluetooth.com/Pages/Bluetooth-Smart.aspx

## Slide 4: Overview (cont.):
The Punch Through Design Bean:
3-axis accelerometer
Temperature sensor
RBG LED
CR2032 Battery Powered
Atmega 328p 8mhz, 3V
6 digital I/O pins, 2 analog
Bluetooth LE Peripheral (wireless programming)
Supports OSX, iOS, and Win 8
Android coming soon!
https://punchthrough.com/bean/
Our commitment to BLE

## Slide 5: Developing Accessories
Your Accessory
Pet Tutor Mobile App
Pet Tutor Feeder

## Slide 6: Developing Accessories
  Arduino Code to Trigger a Feeder:
  Serial.write("CMD-ACCESSORY-FEED");
  OR
  Bean.setScratchNumber(5, 1);

## Slide 7: Connectivity though the Pet Tutor App

## Slide 8: Submitting to Mini-app Store
To get this level of feedback you must go to Arduino’s preferences and select:

## Slide 9: iOS App Development for Pet Tutor
  iOS Code to Trigger a Feeder:
[bean sendSerialString:@"CMD-FEED"];
  OR
  int feedValue = 1;
  [selectedBean setScratchBank:5 data:
  [NSData dataWithBytes:&feedValue length:sizeof(feedValue)]];

## Slide 10: GitHub Introduction
Demos Available At:
https://github.com/PetTutor/PetTutor-SDK-Demos
Git Hub Help:
https://git-scm.com/book/en/v2/Getting-Started-Git-Basics
https://www.youtube.com/watch?v=0fKg7e37bQE

## Slide 11: Questions?